## Slide 1: Compact Single-Turn Coupled Inductor for MHz-Range Buck Converters with Zero-Voltage Switching
Adrian Keil1, Gean Maia de Sousa2, Vincent Lorentz³, Thomas Heckel1, Marcelo Lobo Heldwein2
1 Fraunhofer Institute for Integrated Systems and Device Technology IISB, 2 Chair of High-Power Converter Systems, Technical University of Munich
3 Chair of Electronics for Electrical Energy Storage, University of Bayreuth
June 2, 2026 - O6-5-03
May 31 - June 4, 2026

## Slide 2: Table of Contents
Introduction to the Coupled Inductor Buck Converter
  Working Principle
  Modelling using the Transformer Model
  Effects of Coupling
Inductor Design
  Potential geometries
  Influence of coupling on the flux distribution
  Air-Gap and Winding Optimization
  Design Comparison
Experimental Prototype
Conclusion

## Slide 3: Introduction – Working Principle
Negative Coupling
Positive Coupling
Same Modulation as 2ph Buck
Coupling causes change of the slopes when other leg is pulled to vin
Zero-Voltage-Switching turn-on

## Slide 4: Introduction – Modelling using the Transformer Model
Modelling the coupled inductor as an ideal transformer and two inductors
  Voltages across the two inductors become independent!

## Slide 5: Introduction – Effects of Coupling
Modelling the coupled inductor as an ideal transformer and two inductors
  Voltages across the two inductors become independent!
k
0
-1
1
Lout
Lm
Lself

## Slide 6: Introduction – Effects of Coupling
Modelling the coupled inductor as an ideal transformer and two inductors
  Voltages across the two inductors become independent!
k
0
-1
1
Lout
Lm
Lself

## Slide 7: Inductor Design – Potential Geometries
Investigation of 4 different designs
  (a) and (b): Coupled
  (c) and (d): Uncoupled
Design Goals:
  Lself ≈ 70 nH
  -0.2 < k < -0.4
  Hdc < 40 A/m
  Pcore < 500 mW/cm³
(a) Double-PQ with Dual Air Gap
(b) Four-Pole with Dual Air Gap
(c) Modified EE
(d) Vertical Gap
Additional Air Gap

## Slide 8: Inductor Design – Flux Distribution
Different Flux-Path for DC and Fundamental
Pos. Coupling: High DC-Flux but low AC
Neg. Coupling: Low DC-Flux but high AC
0 |  | 20 |  | 40 |  | 60 |  | 80 |  | 100 | 
B[mT]
Neg. Coupling DC
Neg. Coupling Fundamental
Pos. Coupling Fundamental
Pos. Coupling DC

## Slide 9: Inductor Design – Air-Gap and Winding Optimization
Current crowds in areas of large H-field
Dual Air-Gap improves field distribution
Different winding widths avoid areas of high H-field

## Slide 10: Inductor Design – Comparison between Geometries
Coupled Designs are smaller.
Four-Pole Structure perfoms best while having the lowest copper-loss.
(a) Double-PQ with Dual Air Gap
(b) Four-Pole with Dual Air Gap
(c) Modified EE
(d) Vertical Gap

## Slide 11: Experimental Prototype – Build
45 x 29 x 9.5 mm

## Slide 12: Experimental Prototype - Measurements
Power density: 80 kW/L (1300 W/in³)
Boxed volume: 12.4 cm³
Input ripple: <250 mV Output ripple: <150 mV
Maximum efficiency: 96.3% at 550 W.
Soft-switching at all loads with variable frequency

## Slide 13: Conclusion
Transformer model provides intuitive understanding of 2-phase coupled inductors
Benefit of coupled inductors: Smaller core
  Positive Coupling is beneficial in most cases as it reduces AC flux
  Negative coupling when DC-flux matters (high-frequency materials). Reduces core size by 50% in this case.
Dual air gaps and stepped conductor widths improve current distribution
  30% reduction in copper loss
Experimental prototype: 80 kW/L (1300 W/in³) at 1 kW output and 96.3% peak efficiency.

## Slide 14
CONTACT US
Adrian Keil1, Gean Maia de Sousa2, Vincent Lorentz3, Thomas Heckel1, Marcelo Lobo Heldwein2
May 31 - June 4, 2026
1 Fraunhofer Institute for Integrated Systems and Device Technology IISB, 2 Chair of High-Power Converter Systems, Technical University of Munich
3 Chair of Electronics for Electrical Energy Storage, University of Bayreuth

## Slide 15: Presentation Guidelines: Format
Total duration of presentation is 20 minutes, 15 minutes for presentation and 5 minutes for Q&A.
Limit your presentation to 15 slides and 20MB.
The presentation must not have ‘Confidential’ or ‘Proprietary’ tags.
File format must be Microsoft pptx or Adobe pdf for presentation and pdf only for downloadable proceedings.
  Authors must submit an Adobe version of their presentation file which is verified for conversion accuracy (pptx  pdf).
Slide size must be Widescreen(16:9) and follow this pptx template.
The footer on the:
  title slide must include Presentation Number.
  other slides must only include the slide number.

## Slide 16: Presentation Guidelines: Font Sizes
Recommended minimum Arial font sizes
Titles: 32
Sub-Titles: 28
Major Bullets: 24
  Indented Bullets: 20
Text on graphs, figures,…: 18

## Slide 17: Inductor Design – Potential Geometries
Investigation of 4 different designs
  (a) and (b): Coupled
  (c) and (d): Uncoupled
Merged into 2d Design
In reality: Always round limbs
(a) Double-PQ with Dual Air Gap
(b) Four-Pole with Dual Air Gap
(c) Modified EE
(d) Vertical Gap
Additional Air Gap
Design Goals
TCM under full load at 1.5 MHz
  Approx. 70 nH
Coupling-factor of -0.2 to -0.4
Constraints
Maximum Hdc of 40 A/m
Maximum Pcore of ~500mW/cm^3